## Slide 1
Green Rebuild Initiative
Facilitating 100% Electric, Net Zero Energy Homes, featuring Solar Microgrid Resilience and Engineered for Extreme Weather

## Slide 2: Meet the Team
Craig Lewis, Executive Director
Founder of Clean Coalition, a nonprofit organization dedicated to accelerating the transition to clean energy and a modern grid.
Lollie Kuhl, Design Lead
Architectural designer focused on empowering homeowners with actionable guidance for rebuilding sustainably.
Haley Weinstein, Communications Lead
Communications lead for community outreach and corporate partnering.
John Bello, P.E., Real Estate Development Lead
Professional Engineer and experienced Real Estate Developer assisting the team with construction cost estimating and project management.
Gregory Young, Director of Programs
Leveraging his expertise to conduct sophisticated analyses for Solar Microgrid and Community Microgrid projects.

## Slide 3
Green Rebuild Initiative
Mission:
The Green Rebuild Initiative (GRI) aims to facilitate sustainable and resilient rebuilds through “Super Green” home designs, featuring 100% Electric Net Zero Energy (NZE) designs, supported by Solar Microgrids – for unparalleled resilience. The new homes will also be built with non-toxic materials and be engineered to withstand extreme weather events.
Plan:
              Identify Homeowners
              Facilitate Design
              Perform Load Analysis and Size Solar + Storage
              Streamline Permitting
              Coordinate with Contractors
              Repeat to develop Super Green neighborhoods!
Notes: 3

## Slide 4: Current Collaborators
Architects
  Altadena Collective
    Tim Vordtreide
    Chris Corbett Design
  Uriu Architecture: Scott Uriu
  Joubert Homes: Steffen Andrews
  Bildsten Arch: Ellen Bildsten
  Union Studios: Ben Willis
  Lance Collins: NOMA
  Garcia Architecture: Elisa Garcia
Landscape Architects
  Kiesel Design: Jack Kiesel
General Contractors
  Allen Construction: Dennis Allen
  Williams Homes: Patrice Queensberry
  Best Tech Contracting: Jason Scheurer
Prefab/Modular Manufacturers
  Plant Prefab: Steve Glenn
  Joubert Homes: Darin & Steffen
  ReMo Homes: Ryan Blowers/ Vamsi Kotla
  BPublicPrefab
Other Collaborators
  Mayor of LA: Karen Bass
  Ben Stapleton: USGBC LA
  Desert Estate Development: John Pedalino
  Taft Office: Margie Taft
  Box Power: Fallon Vaughan
  Steadfast LA: Rick Caruso
  Permacity Foundation: Jonathan Port
  California Home+Design: Lauren Michele
  Direct Relief
  Habitat for Humanity

## Slide 5: Community Engagement
State of California
  Elena Kounalakis - Lt. Governor Cali
City of Los Angeles
  Steadfast LA
  LA Rises
  USGBC-LA
  Mayor's Office
  Kathryn Barger - County Supervisor
  LA Sentinel
Altadena
  Altadena Collective
  Altadena Rebuild Coalition: NOMA
  Altadena Chamber of Commerce
  Altadena Heritage
  Altadena Green
  Altadena Strong
Pacific Palisades
Resilient Palisades
Palisades Recovery Coalition
Pacific Palisades Community Rebuild
Pacific Palisades Preservation Coalition (PPPC)

## Slide 6: Conceptual Design: Exterior

## Slide 7: Conceptual Design: Interior

## Slide 8: Timeline
Conceptual Design: Architect
  Finalize home size:
      Square Footage
      Orientation
      # of Bedrooms
      # of Bathrooms
  Develop Conceptual Rendering (4-6 weeks)
  Clean Coalition (2-4 weeks):
    Design Solar Array + Battery System
      Size System for Microgrid Resilience
      Economic Analysis
Design Development: Architect
  SD: Schematic (2-4 Mo.)
      Site Survey (1-2 Weeks)
      Submit for Permit Review (4-6 Weeks)
  CD: Construction Documents (1-2 Mo.)
Construction Schedule: GC
  Foundation (1-2 Month)
  Utility Tie-Ins (4-6 Weeks)
  Framing (1-2 Months)
  MEP (3-4 Months)
  Interior Finishes (3-4 Months)
  Exterior Finishes (1 Month)
  Certificate of Occupancy (2-4 Weeks)
Opportunity for PreFab or Modular Construction

## Slide 9: GRI - Overview
Super Green
        100% Electric
        Net-Zero Operational Energy
        Community Microgrid
Energy Efficiency
  Passive House Design
  High-Performance Insulation
  Blower Door Testing
Extreme Weather Resilience
  Extreme Heat
  Smoke Protection
  Wildfire Resilient
Healthy Development
  Low Embodied Carbon
  Low Operational Carbon
  Indoor Air Quality
  ILFI Red-list Free Materials
  Thermal Comfort

## Slide 10
Super Green
What is ”super green”?
1. 100% electric (no gas service to the home and ideally be an all-EV household).
2. Hosts enough solar to achieve Net Zero Energy (will require about 35 solar panels for a typical 2,500 square foot all-electric home with about 10,000 miles of home EV charging per year).
3. Includes a Solar Microgrid that combines the solar to a battery.

## Slide 11
Specifications
Mechanical and Plumbing
  Heat Pump: Mitsubishi Hyper-Heating H2i
  ERV: Broan Model: B130E65RT
  Air Purifier: Lifebreath TFP3000HEPA
  Thermostat: Ecobee
  Water Heater: AO Smith 900 Series (50 Gal)
Lighting
  Light Bulbs
    Interior: Bulbrite LED (776774)
    Exterior: Bulbrite LED (778672)
  Fixtures
    Energy Star Certified
    Exterior: DarkSky Compliant
  Controls/Sensors: Lutron
    Occupancy
    Vacancy
Super Green: 100% Electric
Notes:     Sealed Ducting, No Flex Duct (G90 Zinc) w/ R6 Insulation
    Wall and Ceiling Registers - Titus

## Slide 12: Super Green: 100% Electric
Appliances
  Bosch Range - 30" HIS8055U
  Broan Vent Hood (BBN1243SS)
  Bosch Microwave (HMB57152UC)
  Bosch Refrigerator - 21 cf (B36CT80)
  Bosch Dishwasher - 24“ (SHX65CM5N)
  LG All-in-One Washer/Dryer (WM6998HBA)
  HomeFlex Level 2 EV Charger (J1772)
Induction Cooktops
100% Electric
Energy Efficient

## Slide 13
Solar (Photovoltaic: PV)
CalGreen Title 24 Energy Code: Solar required for all new homes
Traditional
  1,500sf = 4kW (10 Solar Panels)
  2,500sf = 7kW (16 Solar Panels)
Net-Zero
  1,500sf = 10W (24 Solar Panels)
  2,500sf = 15kW (35 Solar Panels)
Battery Storage
  Store Solar during Day and use at Night
  Back Up Generator
Super Green: Net Zero
Notes: Beyond concrete
Xeroscape
Hot Roof (No Vents)
Minimal Eaves
Compact Design
Heat Treated Wood Siding
Stucco
Metal Roof
NuWool or TimberHP Insulation
EcoCocon - Straw panel (2hr Rating)
Pro Clima Mento - Air Barrier
Tempered Windows
Class A Rated Deck Materials

## Slide 14: Super Green: Net Zero
Net Zero Energy (NZE) a building produces as much renewable energy on-site as it consumes over the course of a year
Notes: Beyond concrete
Xeroscape
Hot Roof (No Vents)
Minimal Eaves
Compact Design
Heat Treated Wood Siding
Stucco
Metal Roof
NuWool or TimberHP Insulation
EcoCocon - Straw panel (2hr Rating)
Pro Clima Mento - Air Barrier
Tempered Windows
Class A Rated Deck Materials

## Slide 15: Super Green: Net Zero
A typical 2,500 sq ft all-electric house that provides about 10,000 miles of home EV charging annually will need about 15kW of solar to achieve Net Zero Energy (NZE), which requires about 35 standard-sized solar panels, requiring about 700 sq ft of clean (no protrusions) south-facing roof surface.
Importantly, achieving Super Green for a new 2,500 sq ft house adds about $80k to the construction cost, but about half of that can be recovered via tax benefits, rebates, and other incentives -- and the net investment will generally earn a 10%+ tax-free, risk-free return-on-investment (ROI), via reduced energy bills. There is no other type of investment anywhere that provides such a high return for what is essentially equivalent to a long-term certificate-of-deposit (CD) that pays a 15%+ annual-percentage-rate (APR).
Notes: 15

## Slide 16: Super Green: Net Zero
The importance of south-facing rooftops:
Notes: 16

## Slide 17: Super Green: Solar Microgrid
Off-Peak Period
Power from Sun
During the day the home draws power from its solar array and charges the home battery.
Peak Period
Power from Battery
Power is drawn from the home’s battery, and Peak Utility-based costs are avoided
© Sonnen
Notes: Operate independently from the utility company

## Slide 18: Super Green: Solar Microgrid
© The Climate Center
Power Outage
Off-Grid Mode
During a planned and/or unexpected power outage, homeowners can shift consumption to Critical Loads and consume energy entirely from their solar + battery system. Critical Loads include only essential appliances and circuits, (HVAC, Refrigerator, Microwave, WiFi, fire-life-safety devices and select outlets).
© Sonnen
Grid Service Request
Earn Credits
Homeowner can earn credits from the utility company by providing excess power during a Grid Service Request. These credits can be used to offset future utility charges
Notes: Operate independently from the utility company

## Slide 19: Super Green: Solar Microgrid
VOR123: Value of Resilience
Tier 1: Mission-critical, life-sustaining loads that warrant 100% resilience — usually about 10% of a facility’s total load.
Tier 2: Priority loads that should be maintained as long as doing so doesn’t threaten ability to maintain Tier 1 loads — usually about 15% of the total load.
Tier 3: Discretionary loads that should be maintained only when doing so does not threaten Tier 1 and Tier 2 resilience — usually about 75% of the total load.

## Slide 20: Energy Efficiency: Passive House
Passive House Design
  Up to 90% Reduction in Energy Demand
  Triple-paned Windows
  Superior Indoor Air Quality
  Reduced Size of Mechanical Equipment
Passive House is the pinnacle standard for energy efficiency. Incorporating these principles into the home’s design ensure the maximum benefit for occupancy health, well-being and energy cost savings.
Notes: Pinnacle of Energy of Efficiency: Passive House design, originating in Germany, maximizes energy efficiency through super-insulation, airtight construction, and heat recovery ventilation to minimize heating and cooling needs.

## Slide 21
Conventional
Foundation = R5
Floors = R10
Wall Assembly = R10
Roof Assembly = R20
Passive House
Foundation = R10
Floors = R20
Wall Assembly = R30
Roof Assembly = R50
High-Performance Insulation
Energy Efficiency: Insulation
Note: High-performing insulation reduces the energy demand stressed on the HVAC system, creating a tremendous long-term cost saving opportunity for the homeowner.
Warning: likely to contain formaldehyde, VOCs, titanium dioxide, PFAS, glass fibers, phenol, heavy metals and other toxic chemicals.
GRI homes will be built with non-toxic materials.
See the Healthy Materials section at the end of this presentation for more info on ILFI’s Red List Free materials

## Slide 22
Blower Door Test
Conventional Home (Code-Built)
  ACH50 Range: 3.0 to 7.0
LEED Silver Home (Standard “Green” Home)
  ACH50 Range: 1.5 to 3.0
Passive House (Super Green Home)
  ACH50 Range: ≤ 0.6
Blower Door Tests are conducted on each home to measure air tightness and identify leaks in the home’s exterior envelope. These leaks are then sealed prior to homeowner occupancy.
Note: Air Changes per Hour (ACH)
Energy Efficiency: Blower Door Test
Notes: Pressurize the home, creating an air difference between inside & outside equal to 50 Pascals (ACH50) [~1lb/sf]
The fan pulls air out of the house
Air pressure is lowered, causes air to be drawn into the building through leaks in the building envelope
ACH = The Qty of Home Air Volumes moved in One Hour

## Slide 23: Extreme Weather Resilience: Extreme Heat
Extreme Heat
Notes: Beyond concrete
Xeroscape
Hot Roof (No Vents)
Minimal Eaves
Compact Design
Heat Treated Wood Siding
Stucco
Metal Roof
EcoCocon - Straw panel (2hr Rating)
Tempered Windows
Class A Rated Deck Materials (IPE)
WUI: Wildland Urban Interface
Trees no closer than 10’ from home

## Slide 24: Extreme Weather Resilience: Extreme Heat
Extreme Heat
⚡ HIGH HEAT EVENTS STRAIN CALIFORNIA’S RESIDENTS & ELECTRIC GRID
1. Skyrocketing Demand for Air Conditioning
On hot days, there is a massive peak in electricity use due to widespread use of air conditioning.
This leads to the risk of blackouts or brownouts when demand exceeds supply.
2. Reduced Efficiency of Power Infrastructure
Transmission lines lose efficiency in high heat, which reduces their capacity to deliver electricity.
Some gas plants also become less efficient or must throttle down to avoid overheating.
3. Higher Risk of Heat Stroke
Prolonged exposure to high temperatures combined with dehydration leads to the body’s temperature regulation system failing.
Who’s at Risk: Elderly individuals, infants, and people with chronic illnesses (especially heart disease or diabetes).
🧊 COMFORT + RESILIENCE = STAYING COOL
A homeowner in a Passive House-certified, net-zero energy home with battery backup is vastly more prepared to withstand a heatwave because:
The house stays cool for long periods without active cooling thanks to thermal mass, insulation, and air sealing.
When cooling is needed, a high-efficiency mini-split and heat pump system can operate with minimal energy use.
Battery storage ensures that even during blackouts, the home remains livable.
Utility bills stay low or net-positive, freeing up income during high-price periods.
Notes: Beyond concrete
Xeroscape
Hot Roof (No Vents)
Minimal Eaves
Compact Design
Heat Treated Wood Siding
Stucco
Metal Roof
EcoCocon - Straw panel (2hr Rating)
Tempered Windows
Class A Rated Deck Materials (IPE)
WUI: Wildland Urban Interface
Trees no closer than 10’ from home

## Slide 25: Extreme Weather Resilience: Wildfire
USGBC Wildfire Defense Toolkit
Defensive Perimeter
Class A Materials
Hot Roof (Non-Vented)
Tempered Triple-pane Windows
Heat Resistant Siding
Build back better once
Timber HP: Class A (2-Hr Rated)
Hot air and gases are deflected out away from the building
Notes: Beyond concrete
Xeroscape
Hot Roof (No Vents)
Minimal Eaves
Compact Design
Heat Treated Wood Siding
Stucco
Metal Roof
EcoCocon - Straw panel (2hr Rating)
Tempered Windows
Class A Rated Deck Materials (IPE)
WUI: Wildland Urban Interface
Trees no closer than 10’ from home

## Slide 26
Fire Wise Design
Note: By using Class A materials for siding, insulation, decking, and other exterior components, the home can achieve the same 2-Hour fire rating as a home with concrete walls, without the high embodied carbon impact.
2-Hour Fire Rating
2-Hour Fire Rating
Build a fortress without it looking like a fortress
Extreme Weather Resilience: Wildfire
=
Notes: Beyond concrete
Xeroscape
Hot Roof (No Vents)
Minimal Eaves
Compact Design
Heat Treated Siding
Stucco
Metal Roof
NuWool or TimberHP Insulation
EcoCocon - Straw panel (2hr Rating)
Pro Clima Mento - Air Barrier
Tempered Windows
Class A Rated Deck Materials

## Slide 27
Smoke Protection: Air Barrier
🔥 HOW IT PROTECTS AGAINST WILDFIRE SMOKE
Monolithic TEEE membrane: Unlike microporous wraps (like Tyvek), the Mento series uses a continuous polymer layer that physically blocks fine particles like wildfire smoke (PM2.5 and PM10).
Highly vapor-open: Allows interior moisture to escape, protecting your wall assembly from condensation and mold.
Windproof and waterproof: Stops wind-driven rain and air leaks, increasing thermal performance.
UV and heat resistant: Can be left exposed for a time during construction and remains stable in extreme heat.
Extreme Weather Resilience: Smoke Protection
Notes: Strategic placement of windows and shading to maximize passive solar heating in winter while minimizing overheating in summer.
Super Insulated
Triple-paned windows and well-insulated doors
A continuous air barrier reduces uncontrolled air leakage, improving energy efficiency and indoor air quality.

## Slide 28: Healthy Development
Low Embodied Carbon
Operational Carbon
Indoor Air Quality
Healthy Materials
  Human Health
  Environmental Health
Thermal Comfort

## Slide 29: Healthy Development: Low Embodied Carbon
Embodied Carbon: all carbon expended during raw material extraction, manufacturing and transportation to the construction site (Cradle-to-Gate).
This example compares the same style home built with sustainably-sourced materials vs. a conventionally built home of the same size.
© Thrive Collaborative

## Slide 30: Healthy Development: Low Operational Carbon
© Thrive Collaborative

## Slide 31: Healthy Development: IAQ
Indoor Air Quality
© Thrive Collaborative
ERV (Heat Exchanger): Brings in fresh air while managing humidity and removing indoor pollutants like CO₂ and VOCs.
Air Purifier: In-line Air Purifier provides enhanced protection against wildfire smoke and airborne viruses.
MERV 13 Air Filter: Captures dust, pollen, and mold spores to reduce allergens and improve respiratory health.
Red List Free Materials: Eliminates harmful chemicals, reducing off-gassing and supporting long-term occupant health.

## Slide 32: Healthy Development: Thermal Comfort
Thermal Comfort
© Thrive Collaborative
Home Orientation: A south-facing orientation maximizes sun exposure during winter, capturing free heat from the low-angled sun.
Summer Condition: Roof overhangs or shade structures block high summer sun, keeping interiors cool without mechanical cooling.
Winter Condition: With no shading, the low winter sun penetrates deep into living spaces, naturally warming the home during cold months.
Triple-Paned Windows: High-performance windows reduce heat loss while allowing sunlight in, enhancing both insulation and passive heat gain.
Ecobee Thermostat: A smart thermostat that optimizes indoor temperatures by learning usage patterns and adjusting heating based on real-time conditions, maximizing comfort and energy efficiency.

## Slide 33: Healthy Development: Materials
Living Future Red List
The Living Future Red List is a list of chemicals representing the “worst in class” substances prevalent in the building industry that pose serious risks to human health and environmental health.
Hazards include cancer, reproductive toxicity, acute or chronic organ toxicity, endocrine disruption, environmental persistence, bioaccumulation, ozone depletion, and others.
Homes built as part of GRI will target procurement of exclusively Red List Free material.
https://living-future.org/red-list/

## Slide 34: Healthy Development: Materials
Living Future Red List
Chemical | Where It’s Found | Environmental Impacts | Human Health Impacts
Asbestos | Insulation, flooring, roofing, cement board | Persistent in the environment, hazardous waste | Causes lung cancer, mesothelioma, and asbestosis
Formaldehyde | Composite wood, insulation, adhesives, cabinetry | Air pollutant, contributes to smog formation | Respiratory irritant, probable human carcinogen
PVC (Polyvinyl Chloride) | Vinyl flooring, pipes, wall coverings, windows | Toxic byproducts during manufacturing and disposal (dioxins) | May contain phthalates and heavy metals; endocrine disruptor
Phthalates (e.g., DEHP) | Vinyl products, sealants, adhesives, wall coverings | Persistent, bioaccumulative; toxic to aquatic organisms | Hormone disruption, developmental and reproductive toxicity
Flame Retardants (e.g., PBDEs) | Insulation, upholstery, electronics casings | Persistent organic pollutants; accumulate in wildlife | Thyroid disruption, neurodevelopmental harm, possible carcinogen
Halogenated Solvents | Paint removers, cleaners, degreasers, adhesives | Air and water pollutant; hazardous waste | Neurotoxic, liver/kidney damage, suspected carcinogen

## Slide 35: Healthy Development: Materials
Living Future Red List
Chemical | Where It’s Found | Environmental Impacts | Human Health Impacts
Cadmium | Pigments, coatings, plastic stabilizers | Soil and water contaminant; bioaccumulative in food | Kidney damage, respiratory issues, known carcinogen
Lead | Paint, plumbing, roofing materials | Long-lasting soil/water contaminant; harmful to wildlife | Neurotoxic, affects child development, cardiovascular effects
Mercury | Fluorescent lighting, switches, thermostats | Bioaccumulative in fish; persistent in water systems | Nervous system damage, cognitive impairment, kidney damage
Isocyanates (e.g., MDI, TDI) | Spray foam insulation, paints, sealants | Contribute to smog, hazardous waste | Respiratory sensitizer, asthma, skin and eye irritation
PFAS | Paints, Stain-resistant carpets, sealants, coatings, membranes | Extremely persistent ('forever chemicals'), water pollution | Hormone disruption, cancer, immune system effects
VOCs | Paints, sealants, adhesives, flooring, cabinetry | Ground-level ozone (smog) formation, indoor air pollution | Eye/nose/throat irritation, liver/kidney damage, carcinogenic

## Slide 36
Material Specifications
Foundation
  Concrete with Low GWP
Framing
  FSC Certified Lumber
Roofing
  26g Standing Seam Metal
Insulation
  TimberHP, Rockwool, UltraTouch Denim or NuWool
Drywall
  USG Ecosmart
Flooring
  FSC Red Oak w/ Rubio Monocoat
  Forbo Marmoleum
Tile
  DalTile or Fireclay
Air Barrier
  Pro Clima Mento
Plumbing
  PEX, IBEX and ABS
Windows and Doors
  Elitfonster Triple Paned
Countertops
  Dekton or Reclaimed Wood
Paint
  Benjamin Moore Ultra Spec
Siding
  Stucco and/or Metal
Decking
  Bison IPE Class A Wood
Cabinets
  FSC Maple and MDF
Healthy Development: Materials

## Slide 37: Conclusion
Conclusion: Clean Coalition is committed to ensuring communities achieve resilient energy solutions and an unparalleled trifecta of economic, environmental, and resilience benefits.
Our plan bridges innovation and community action, turning the tragedy of the fires into an opportunity to create a sustainable, resilient, and thriving Palisades.
Together, we can lead the way toward a future built on renewable energy and environmental responsibility.

## Slide 38: Conclusion